## Slide 1: Computer Network Lab Review of Lab2 & Introduction of Lab 3
4/6/2021
王智彬

## Slide 2
User 137.196.7.23
want to Ping 137.196.7.88
  Source IP: 137.196.7.23
  Destination IP: 137.196.7.88
  Source MAC: 71-65-F7-2B-08-53
  Destination Mac: ?
Its MAC address is needed to deliver the data
On LAN, ARP is used get a host/router’s MAC given its IP address
MAC Address Resolution Problem

## Slide 3
ARP (Address Resolution Protocol)
  Map IP address to MAC address
  192.168.1.2 -> 00-15-C5-49-04-A9
  Only works in a LAN
Compare: DNS (domain name system)
  Map domain name to IP address
  Baidu.com -> 220.181.38.148
Hub in lab1 or switch in lab2 connects the client and the server，together they form a LAN.
Address Resolution Protocol

## Slide 4
Every host maintains an ARP table
  List of (IP address  MAC address) pairs
Sender
  Looks into local cache first, if none
  Constructs ARP request, insert <sender IP, sender MAC, destination IP>
  Broadcasts using MAC frame
  Caches destination’s <MAC, IP> pair with timestamp
Receiver
  Checks the destination IP, if OK
  Constructs ARP reply, insert <destination IP, destination
MAC>
  Sends to sender MAC using MAC frame
  Caches sender’s <MAC, IP> pair with timestamp
ARP Procedure

## Slide 5
Computer A:
IP: 129.25.10.72
MAC: 49:72:16:08:64:14
Computer B:
IP: 129.25.10.97
MAC: 49:72:16:08:80:70
Computer C:
IP: 129.25.10.81
MAC: 49:17:92:96:96:96
Server/Router R IP: 129.25.10.11
MAC: 49:78:21:21:23:90
MAC address of 129.25.10.11 ?
Requested by: 49:72:16:08:64:14
(129.25.10.72)
ARP-Request to MAC FF:FF:FF:FF:FF:FF (Broadcast)
1
Reply: 129.25.10.11
(49:78:21:21:23:90)
Requested by: 129.25.10.72
ARP-Reply to MAC 49:72:16:08:64:14
2
ARP Cache Table
（Will time out in a few minutes）
Illustration of ARP

## Slide 6: ARP in Lab2
It is broadcast when we send an ARP request, while using the exact mac address when we receive an ARP reply.

## Slide 7: Confusion in Lab2
Why is this ARP request not broadcast?
Why do we need an ARP request when the mac address already exists in the table?
It is because of ARP's Unicast Poll mechanism. When an entry in ARP table timeout, the system will choose to send an ARP Request of MAC address to ask whether the MAC address and IP address of the other party have changed, to update the table entry, rather than just using the way of broadcast.
http://114.212.81.3:8899/d/14-mac-arp-request

## Slide 8
host
host DNS
...
host
host
host
...
router
router
5.6.7.0/24
1.2.3.48 1.2.3.156
1.2.3.19
router
Look up the MAC address of the first hop router
  1.2.3.48 uses ARP to find MAC address for first-hop router
1.2.3.19 rather than ultimate destination IP address
How does the red host know the destination is not local?
  Uses netmask (discovered via DHCP)
How does the red host know about 1.2.3.19?
  Also DHCP
Default: gateway
1.2.3.0/24 (255.255.255.0)
75
What if the destination is remote?

## Slide 9
IP1|MAC1
IP2|MAC2
IP3|MAC3
IP4|MAC4
IP5|MAC5
IP6|MAC6
Head
MAC Frame |  |  |  | IP Head |  |  | 
… | SA | DA | … | … | SA | DA | …
… | MAC1 | ? | … | … | IP1 | IP6 | …
H
ead
MAC Frame |  |  |  | IP Head |  |  | 
… | SA | DA | … | … | SA | DA | …
… | MAC3 | MAC4 | … | … | IP1 | IP6 | …
H
ead
MAC Frame |  |  |  | IP Head |  |  | 
… | SA | DA | … | … | SA | DA | …
… | MAC5 | MAC6 | … | … | IP1 | IP6 | …
Use ARP to find the next-hop MAC!
MAC2
You need to implement ARP reply in lab3
We will consider ARP request in lab4
Example: PC1 Ping PC2

## Slide 10: Task of Lab3
After receive an ARP request, construct an ARP reply
  Details in the ARP Procedure (page 4) and the lab manual (https://pavinberg.gitbook.io/nju-network-lab/ipv4-router/lab-3/handle-arp-request)
Cache ARP table
  Avoid having to construct and send an ARP request to obtain the same information, we will explain the detail reasons in lab4.
DDL:4/21/2021

## Slide 11
Q & A